## Slide 1
S-Board OTA Firmware Update System
CAN-FD Over-The-Air Updates for TI C2000 F28P55x
GEN3 Power Distribution Unit | Delta Electronics
Author: Parthasarathy M

## Slide 2
The Problem
Updating 100+ deployed S-Boards:
Physical access to each board
JTAG debugger connection
CCS installed on field laptop
15+ minutes per board
Risk of bricking on power loss
What we need:
Remote update over CAN bus
No JTAG, no CCS needed
~30 seconds per board
Brick-proof design
Professional GUI tool

## Slide 3
Dual-Bank OTA Architecture
Flash memory layout on F28P55x
BANK 0 (0x080000)
Sectors 0-7: BOOT MANAGER
Flashed via JTAG once
NEVER erased by OTA
Sectors 8-127: APPLICATION
Running firmware
Updated by boot manager
via Bank 2 copy
BANK 2 (0x0C0000)
128 sectors
OTA STAGING AREA
New firmware received
over CAN-FD
written here first
COPY
<<<<<<
BANK 3 (0x0E0000) — Boot Flag: 0xA5A5 / 0x5A5A + size + CRC

## Slide 4
OTA Protocol — 4 Steps
1
1. ERASE
CMD_FW_START (0x30)
Erase Bank 2 (128 sectors)
Wait ~10s for ACK
2
2. HEADER
CMD_FW_HEADER (0x31)
Send size, CRC, version
MCU parses and ACKs
3
3. DATA
Data frames (ID 6)
64 bytes each, 16/burst
ACK after each burst
4
4. VERIFY
CMD_FW_COMPLETE (0x33)
MCU computes CRC32
CRC_PASS or CRC_FAIL
On CRC_PASS: MCU writes boot flag to Bank 3, resets. Boot manager copies Bank 2 → Bank 0 on next boot.

## Slide 5
Brick-Proof Design
Every failure mode has a safe recovery path
Power lost during Bank 2 write
Boot manager untouched. Boots old FW. Retry OTA.
Power lost during Bank 0 copy
Boot manager retries copy on next boot (flag still set).
CRC mismatch after transfer
Boot manager clears flag, boots old FW. No harm.
CAN bus disconnected mid-transfer
Sender times out. MCU stays on old FW. Retry later.
Boot manager NEVER erases itself. Only a JTAG write to sectors 0-7 can brick the device.

## Slide 6
Professional GUI — 8 Tabs
Manual Control
Step-by-step OTA
Connect, Erase, Header
Data, Verify, Single Frame
MCU Operations
Read/Write boot flag
Read flash, Erase sector
CRC, Reset, Raw CAN
CAN Monitor
Live bus sniffer
All IDs, timestamps
Start/Stop/Clear
CAN Bus
PCAN channel select
Bit timing config
Live bitrate display
Protocol
CAN IDs (6, 7, 8)
Command codes
Response codes
Timing
Burst size, frame size
Inter-frame delay
All timeouts, retries
Header
Magic, image type
Dest bank, entry point
For custom flash layouts
Settings
Dark/Light/System theme
Save/Load settings
Reset to defaults

## Slide 7
Binary Format Fix
hex2000 --image with ROMS directive
BROKEN (hex2000 --binary)
Byte 0: codestart[0] OK
Byte 2: codestart[1] OK
Byte 4: FPUmathTables WRONG!
(should be at byte 16)
Sections concatenated
with NO gaps
Every section after codestart
lands at the WRONG address.
Firmware is SCRAMBLED.
Size: 40,442 bytes (34 short)
FIXED (hex2000 --image + ROMS)
Byte 0: codestart[0] OK
Byte 2: codestart[1] OK
Byte 4: 0xFFFF (fill) GAP
Byte 14: 0xFFFF (fill) GAP
Byte 16: FPUmathTables CORRECT!
Address gaps filled
with 0xFFFF
Every section at the correct
flash address. Works perfectly.
Size: 40,476 bytes (exact)

## Slide 8
Three Critical Bugs Fixed
BUG 1: Flash ops ran from FLASH
boot_manager.c: eraseSector(), programEightWords() in .text (flash).
Flash FSM locks ALL banks during erase — CPU stalls.
FIX: #pragma CODE_SECTION(.TI.ramfunc) on all 5 functions.
BUG 2: Boot flag write failed
fw_image_rx.c: FW_triggerUpdate() ran from flash, called
FW_writeBootFlag() (RAM). Return address in locked flash.
FIX: Both functions .TI.ramfunc. Self-contained Flash API init.
BUG 3: Binary format wrong
hex2000 --binary concatenates sections, destroying address gaps.
Firmware scrambled when copied to Bank 0.
FIX: hex_image.hexcmd with --image + ROMS directive.

## Slide 9
Performance
Specification
─────────────────────────
Firmware size: ~40 KB
CAN-FD data rate: 2 Mbps
Frame size: 64 bytes
Total frames: ~633
Burst size: 16 frames
Inter-frame delay: 1 ms
CRC algorithm: CRC32 (IEEE 802.3)
Timing Breakdown
─────────────────────────
Bank 2 erase: ~10 sec
Data transfer: ~15 sec
CRC verification: ~2 sec
Boot manager copy: ~5 sec
─────────────────────────
TOTAL: ~32 sec
vs JTAG: 15+ minutes

## Slide 10
Repository Structure
S-Board-Firmware
github.com/partham20
Application firmware
OTA receiver (fw_image_rx.c)
hex_image.hexcmd
boot_manager
github.com/partham20
Boot manager
Bank 2 → Bank 0 copy
CAN debug telemetry
fw-updater-gui
github.com/partham20
Python GUI + CLI sender
Documentation
Presentation
powercalculation
gitlab.deltaww.com
Primary S-Board repo
Branch: FW_OTA
Internal mirror

## Slide 11
Thank You
Questions?
github.com/partham20/S-Board-Firmware
github.com/partham20/boot_manager
github.com/partham20/fw-updater-gui